INTERNET ADDRESSING

ICANN International Corporation of Assigned Names and Numbers.  A private, nongovernment organization that ensures each user has a unique IP address.

# Four Dotted Quad Fields

## Binary:  32-bit (IPv4) 128-bit (Ipv6) addresses.  Each field = 1 byte.  8 bits = 1 byte

Decimal:  Each quad with a value between 0 (binary 0~field off) and 255 (binary 1~field on)

| INTERNET ADDRESS CLASSES |
| --- |
| Class | 1st byte | 1st bit(s) | Network/Host Portions |
| A | 1-126 | 0 | 8 bits/1 byte 126 networks | 24 bits/3 bytes 16,777,214 hosts |
| 0.0.0.0 to 127.255.255.255 |  |  |
| 0.0.0.0 | Used when computer initializes and requests an IP address. Source address is initially 0.0.0.0 until it is assigned an IP address |
| 10.0.0.0 to 10.255.255.255 | Reserved IP addressing for private internets |
| 127 loopback: Cannot be used as internet address. Allows client/server on same host to communicate. Ideal for testing/troubleshooting (127.0.0.1 localhost) |
| B | 128-191 | 10 | 16 bits/2 bytes 16,384 networks | 16 bits/2 bytes 65,534 hosts |
| 128.0.0.0 to 191.255.255.255 |  |  |
| 172.16.0.0 to 172.31.255.255 | Reserved IP addressing for private internets |
| C | 192-223 | 110 | 24 bits/3 bytes 2,097,152 networks | 8 bits/1 byte 254 hosts |
| 192.0.0.0 to 223.255.255.255 |  |  |
| 192.168.0.0 to 192.168.255.255 | Reserved IP addressing for private internets |
| D | 224-239 | 1110 | MULTICASTING: Not routable. Datagram targeted to a group that is identified by network address only. (no host portion) |
| 224.0.0.0 to 239.255.255.255 |  |
| E | 240-247 | 11110 | EXPERIMENTAL: Reserved for future use. |
| 240.0.0.0 to 247.255.255.255 |  |
| BROADCAST ADDRESSES (255) (Network and host portions cannot be 255) Send messages to all network hosts and are used only as destination addresses. |
| Limited Broadcast 255.255.255.255 | Used for configuring hosts when they boot up. (Not valid for sending and receiving) Can broadcast to obtain an IP address from DHCP or BOOTP servers. |
| Net-directed Broadcast | Used to broadcast to all hosts in a network. Assigned network quad(s) host quad(s) is/are 255 |
| Subnet-directed Broadcast | Broadcast can be sent to all hosts within a subnet. |
| All-subnets-directed Broadcast | Has become obsolete ~ multicasting is preferred. Broadcast can be sent to all hosts within all network subnets. |